## Slide 1: Integer Multiplier
ECE-111 Advanced Digital Design Project
Vishal Karna

## Slide 2: Homework Assignment : Integer Multiplier
Develop SystemVerilog RTL model for N-bit Integer Multiplier
  Develop Finite state machine and state transition diagram for SHIFT and ADD multiplier algorithm
  FSM coding style recommended : Single always block with non-blocking assignment statements within always block.
  Synthesize integer multiplier design for parameter N=4 and run simulation using testbench provided
  Review synthesis results (resource usage and RTL netlist/schematic)
  Review input and output signals in simulation waveform.
  Assume below mentioned primary port names and SystemVerilog RTL module integer_multiplier.
  Note : FSM code framework is provided in Lab folder with comments to help develop the code.
  Testbench provided has built in checker to ensure design output is expected. See messages in Modelsim transcript window when performing simulation
Primary Ports for integer_multiplier module
  input clock, reset (asynchronous posedge reset)
  Input start (1 cycle pulse generated. Indicates to FSM to start multiplication operation)
  input logic[N-1:0] multiplicand, multiplier
  output logic[(2*N):0] product (result of multiplication includes carry bit as MSB bit)
  output logic done (inidicates that product is available. This is one cycle pulse generated by FSM)
integer_multiplier
clock
reset
product
multiplicand
multiplier
done
start

## Slide 3: Homework Assignment : Integer Multiplier
Report should include :
  SystemVerilog design, State diagram (hand drawn snapshot or Snapshot from Quartus either way is fine)
  Synthesis resource usage and schematic generated from RTL netlist viewer
  Simulation snapshot and explain simulation result to confirm RTL model developed works as a integer multiplier
Reference Output Snapshot
Once Start is ‘1’ multiplicand value 11 and multipler value 13 are loaded in load_reg
Once ‘done’ signal is ‘1’ for single clock cycle, ‘product’ value of 143 is available from multiplier FSM
Since N=4, ie. Inputs are 4 bit values, count value will increment from 00, 01, 10, 11 which indicates 4 stages of ADD/SHIFT operation

## Slide 4: SHIFT And ADD Method to Perform Integer Multiplier
Multiplier : 4’b1101 (13), Multiplicand : 4’b1011 (11), Expected Product = 11 x 13 = 143 (9’b0_1000_0111)
N-bit Multiplier has N stages of SHIFT and ADD round of computation
If Multiplier LSB[0] = 1 Perform ADD of Accumulator + Multiplicand and store back to Accumulator and then perform Right Shift by 1
If Multiplier LSB[0] = 0 Perform Right Shift by 1
Stage-1 | Carry | Accumulator | Multiplier | Operation Performed
0 | 0 | 0 0 0 0 | 1 1 0 1 | Initialize
1 | 0 | 1 0 1 1 | 1 1 0 1 | ADD
 | 0 | 0 1 0 1 | 1 1 1 0 | SHIFT >> 1
2 | 0 | 0 0 1 0 | 1 1 1 1 | SHIFT
3 | 0 | 1 1 0 1 | 1 1 1 1 | ADD
 | 0 | 0 1 1 0 | 1 1 1 1 | SHIFT >> 1
4 | 1 | 0 0 0 0 | 1 1 1 1 | ADD
 | 0 | 1 0 0 0 | 0 1 1 1 | SHIFT >> 1
acc + multiplicand
0 0 0 0 + 1011 = 01011
acc + multiplicand
0 0 1 0 + 1011 = 01101
acc + multiplicand
011 0 + 1011 =1000

## Slide 5: SHIFT And ADD Integer Multiplier Algorithm Summary
Multiplication Process and FSM States :
  IDLE: Wait in this state until Start=1. Then move to INITIALIZE state if input signal Start==1
  INITIALIZE: Multiplicand and multiplier are loaded into a load register and a shift register, respectively;
  TEST: The LSB in the shift register which contains the multiplier is tested to decide the next state. If shift register LSB is ‘1’, then next state is to ADD otherwise next sate is to SHIFT_AND_COUNT
  ADD: the Adder adds previous stage add result with Multiplicand and stores the product to the accumulation result, back to shift register and then the state machine transits to SHIFT_AND_COUNT state
  SHIFT_AND_COUNT: If shift register content is right shifted by 1 bit position. MSB of shift register ‘0’ is entered
  When the counter reaches to N, then next state is DONE stage otherwise next state is TEST state for next stage ADD/SHIFT operation
  DONE: Done signal is asserted to ‘1’ and shift register content is sent to ‘product’ output signal

## Slide 6: Homework Assignment : Integer Multiplier
Quartus Generated State Machine Diagram and State Table for reference purpose
start ==1
if shift_reg[0] ==1
if shift_reg[0] ==0
if count == N
if count < N
Unconditionally transition to IDLE state
Unconditionally transition to TEST state
Note : When FSM transition to DONE state, load “shift_reg” value to “product”
And set done = 1 from separate logic using assign statement

## Slide 7: Block Diagram of Integer Multiplier Using SHIFT and ADD
4-bit Multiplicand Input
4-bit Multiplier Input
Check If shift_reg[0]==1 then ADD operation followed by SHIFT>>1 operation
Check If shift_reg[0]==0 then SHIFT>>1 operation (no ADD operation performed)
4-bit Carry LookAhead Adder
load_reg
(when start=1, Multiplicand loaded to load register)
shift_reg[7:5]
(4 bit adder output without carry out)
shift_reg[3:0]
shift_reg[8]
(Carry out from Adder)
If shift_reg[0] ==1 then ADD operation, Multiplicand input in load_reg is selected by MUX and sent to Carry Look Ahead Adder otherwise select ‘0’ and sent to the input of adder
Second Input to Carry LookAhead adder is the previous stage 4 bit adder result
add_operand2
add_operand1
shift_reg>>1
product = shift_reg[8:0] when done = 1
accumulator

## Slide 8: SHIFT And ADD Integer Multiplier Algorithm Steps Summary
1. Multiplicand Value = 4’b1011 loaded to register
2. Since Initialize shift_reg[0] == 1,
Perform ADD operation
1. Initialize shift_reg[3:0] to Multiplier value 4’b1101
2. Check if shift_reg[0] == 1 ?
4. shift_reg entire 9 bits register right shift by 1
3. Load result of Multiplicand +
Accumulator value to shift_reg[8:5]
3. Load result of Multiplicand +
Accumulator carry out value to shift_reg[8]
1. Initialize accumulator to 4’b000. accumulator is represented as shift_reg[7:4]
1. Initialize carry out bit in shift_reg[8] to 4’b0
2. Select and connect Multiplicand to Carry LookAhead Adder input-1 port
2. Select and connect shift_reg[7:4] which is accumulator value to Carry LookAhead Adder input-2 port
3. Perform ADD operation
At end of stage-0 count, shift_reg = {0, 4’b0101, 4’b1110}, Repeat these steps until count value == N. And end of stage-3 count, final product will be available

## Slide 9: Let’s us do simulation of 4-bit Integer Multiplier using SHIFT and ADD Multiplier Algorithm

## Slide 10: SHIFT And ADD Integer Multiplier Algorithm Example Steps
Multiplicand Value = 4’b1011 loaded to register
1. Initialize accumulator to 4’b0000 accumulator is represented as shift_reg[7:4]
Initialize carry out bit in shift_reg[8] to 4’b0
Step 1 : Initialize registers
N-Bit Counter to 0

## Slide 11: SHIFT And ADD Integer Multiplier Algorithm Example Steps
Since Initialize shift_reg[0] == 1,
Perform ADD operation
Check if shift_reg[0] == 1 ?
Select and connect Multiplicand to Carry LookAhead Adder input-1 port
Select and connect shift_reg[8:5] which is accumulator value to Carry LookAhead Adder input-2 port
Step 2 : Test LSB, check if shift_reg[0] == 1 ?
If ‘1’ then load multiplicand and accumulator (shift_reg[8:5]) bits to multiplier
N-bit counter value is still ‘0’ at end of this step

## Slide 12: SHIFT And ADD Integer Multiplier Algorithm Example Steps
Load result of Multiplicand +
Accumulator value to shift_reg[8:5]
Load result of Multiplicand +
Accumulator carry out value to shift_reg[8]
Perform ADD operation
Step 3 : Perform ADD Operation
N-bit counter value is still ‘0’ at end of this step

## Slide 13: SHIFT And ADD Integer Multiplier Algorithm Example Steps
Step 4 : Perform SHIFT Operation
shifg_reg = shift_reg >> 1
And increment N-bit counter by 1
shift_reg entire 9 bits register right shift by 1
At end of N-bit count==0 stage, value of shift_reg = {0, 4’b0101, 4’b1110}

## Slide 14: SHIFT And ADD Integer Multiplier Algorithm Example Steps
N-bit Counter value is ‘1’
Step 5 : Check if shift_reg[0] == 0 or 1 ?
Check if shift_reg[0] == 0 ?
Do not perform Add
Load operand-1 of adder with value 4’b0000 and do not load multiplicand value
Select Shift Operation
Select and connect shift_reg[7:4] which is accumulator value to Carry LookAhead Adder input-2 port

## Slide 15: SHIFT And ADD Integer Multiplier Algorithm Example Steps
Step 6 : Perform SHIFT Operation
shifg_reg = shift_reg >> 1
And increment N-bit counter by 1
4. shift_reg entire 9 bits register right shift by 1
At end of N-bit count==1 stage, value of shift_reg = {0, 4’b0010, 4’b1111}

## Slide 16: SHIFT And ADD Integer Multiplier Algorithm Example Steps
Step 7 : Check shift_reg[0] == 1 or 0 ?
Step 8 : since since shift_reg[0] == 1 then Perform Add Operation
Step 9 : Perform Shift operation shift_reg >> 1 and then increment N-N-bit counter value
At end of N-bit count==2 stage, value of shift_reg = {0, 4’b0110, 4’b1111}

## Slide 17: SHIFT And ADD Integer Multiplier Algorithm Example Steps
Step 10 : Check shift_reg[0] == 1 or 0 ?
Step 11 : since since shift_reg[0] == 1 then Perform Add Operation
Step 12 : Perform Shift operation shift_reg >> 1 and then increment N-bit counter value
At end of N-bit count==3 stage, value of shift_reg = {0, 4’b1000, 4’b1111}
Since count == 3, set done = 1 and product = shift_reg (9’b0_1000_1111) = 143

## Slide 18: Integer Multiplier Code Development Hint
Define 6 FSM States
For N-bit Integer Divider, ensure size of shift register is = N + N + 1 bits
  N bits to store adder output without carry out in shift register (this is also know as accumulator)
  N bits to store multiplier value
  1 bit to store carryout bit from adder
  shift register format = {carryout, N-bit Adder output, N-bit Multiplier}
Use Carry Look Ahead Adder and Full Adder Module implementation from previous homework assignment

## Slide 19: Integer Multiplier Code Development Hint
Develop FSM code using single always block approach with non-blocking assignment statements within

## Slide 20: Integer Multiplier Code Development Hint
FSM code framework…. Continued
Using assign statement generate output ‘done’ and final ‘product’ value when FSM transitions to DONE state